## Slide 1: FIFO
Literature Survey

## Slide 2: Why FIFO required?
Exchange of data between two different PCBs working at different frequencies
Otherwise slowest component will determine the speed

## Slide 3: What is FIFO?
First In First Out
Ex. Queue at ticket counter

## Slide 4: What is FIFO?(Contd.)
Dual Port Memory
Data Output
Write Logic
Read Logic
Data Input

## Slide 5: FIFO Implementation
Software
  Flexible to requirement change
Hardware
  Speed

## Slide 6: Types of FIFOs
Shift Register
  Fixed number of stored data word.
Exclusively Read/Write FIFO
  Variable number of stored data words
  Timing restrictions - synchronous
Concurrent Read/Write FIFO
  Variable number of stored data words
  No timing restriction – asynchronous
  Two circuits with different frequencies can be connected together without the need of a synchronizing circuit

## Slide 7: Multiple Clock Domain Design
The Clock type, and functions
Moving data across clock domains
Synchronizing interfaces

## Slide 8: The Clock and Reset types
Conceptually, a clock consists of two signals
  an oscillator
  a gating signal
In general, implemented as two wires or digital periodic signal
If ungated, oscillator is running
Whether the reverse is true depends on implementation library—tool doesn’t care

## Slide 9: Moving Data Across Clock Domains
Data moved across clock domains appears asynchronous to the receiving (destination) domain
Asynchronous data will cause meta-stability
The only safe way: use a synchronizer

## Slide 10: Synchronizers:
Good synchronizer design and use reduces the probability of observing meta-stable data
Synchronizers needed for all crossings
Bit synchronizer
Pulse synchronizer
FIFO synchronizer

## Slide 11
Bit synchronizer
Pulse synchronizer
3. FIFO synchronizer

## Slide 12: Synchronizing Interfaces
Hardware approach in clock-domain crossing
  Designers instantiate a module having different clocks for different methods, and connect it up explicitly
Alternative linguistic approach
  To convert an interface from one clock domain to another
  Converts an existing interface to another one of the same type, but on different clock.

## Slide 13: Architecture
D
C
B
A
E
D
C
B
Data
Input
E
Data
output
A
Write
Fall-Through
Read
Latch

## Slide 14: Architecture (Contd.)
Circular FIFO with two pointer

## Slide 15: How it functions?
Ref: Document from Texas Instrument

## Slide 16: Functionality Of Pins
WRITE CLOCK and FULL(active low)
  used to write a data into synchronous FIFO
READ CLOCK and EMPTY(active low)
  The control line READ and the EMPTY are used for reading the data
RESET
  It is used to perform reset operation. On reset, read and write pointer will initialize to zero (pointer will be pointing to start of the memory)

## Slide 17: Functionality Of Pins (Contd.)
INPUT DATA
  The input data pin is used to feed an input data to memory. When clock edge is applied read or write operation are perform on the data.
OUTPUT DATA
  After performing the operation on given input data the data is available on the output pins of the FIFO.

## Slide 18: How it performs read and write?
A FIFO is a First In First Out memory. Data is being shifted in one end and shifted out the other, with the amount of data in the FIFO being allowed to grow up to some maximum limit.
A better way is to use a memory more normally but make it look like a circular buffer by manipulation of the next address to write to and read from.
These addresses live in separate registers, and are often called the read pointer and the write pointer.

## Slide 19: Important consideration in design
Overflow:
  Occurs when the FIFO is full and writer attempts to insert a new data element
Underflow:
  Occurs when the FIFO is empty and reader attempts to retries an element from buffer

## Slide 20: Applications
Packet Buffering :
  Data written into the FIFO can be stored until the system on the output of the FIFO is ready to accept the data.
Frequency coupling:
  FIFO provides frequency coupling, taking data in at one rate and outputting it at another. The input and output data rates of the FIFO being controlled by the discrete Read and Write clock signals.
Bus Matching :
  Data transfer may need to take place between separate digital domains with different bus widths. Here the FIFO acts as a bridge between the domains, channeling the data from

## Slide 21: Advantages
Data Rate Matching
Buffering and bus matching parallel FIFO structure allow formulation of any word size while serial FIFO structure provide a rapid and simple like other structure.
Interchip communication protocol problem is solved by FIFO.
Only circuitry required is to create fast FIFO, control logic, flag logic

## Slide 22: Disadvantages
Noise in signals is caused by switching operation and alteration of memory content
Synchronization circuit is required to synchronize WRITE CLOCK and READ CLOCK

## Slide 23
Thank You !
Any Queries ?