## Slide 1: FIFO Implementation Using FPGA
Guided by:
Dr. Y.V. Joshi
Dr. S.S. Gajre
Industrial Guide:
Mr. Vaibbhav Taraate
Team members:
Mahesh Baraskar
Mukul Lokhande
Pushpak Ghatode
Tejaswini Khairnar
Ratnamala Patil

## Slide 2: Why FIFO required?
Exchange of data between two different PCBs working at different speed
Otherwise slowest component will determine the speed

## Slide 3
What is FIFO?
  First In First Out
Ex. Queue at ticket counter
FIFO Implementation
  Software
  Flexible to change in requirements
  Hardware
  Speed is High

## Slide 4: Types of FIFOs
Shift Register
  Fixed number of stored data word.
Exclusively Read/Write FIFO
  Variable number of stored data words
  Timing restrictions - synchronous
Concurrent Read/Write FIFO
  Variable number of stored data words
  No timing restriction – asynchronous
  Two circuits with different frequencies can be connected together without the need of a synchronizing circuit

## Slide 5: Architecture
D
C
B
A
E
D
C
B
Data
Input
E
Data
output
A
Write
Fall-Through
Read
Latch

## Slide 6: Architecture (Contd.)
Circular FIFO with two pointer

## Slide 7: SPECIFICATIONS
BURST Size : 1.5K bytes
FIFO Size : 1 K bytes
Input Data Pins: 8
Input Pins: 2 (R/W enable)
Output Data Pins: 8
Write Pointer Pins: 10
Read Pointer Pins: 10
Flag Pins: 5 ( EMPTY, FULL, HALF FULL / EMPTY, ALMOST FULL, ALMOST EMPTY)
Reset: 1
Write Clock (100MHz)
Read Clock (33MHz)

## Slide 8: Top Level Diagram:

## Slide 9: Top Level Diagram:
Dual Port SRAM
Write Control
Read Control
Synchronizer
Write enable
Read enable
Read clock
Write clock
Write Data
Read Data
reset
reset
Flag Logic

## Slide 10: Micro Architecture

## Slide 11: Top Level RTL

## Slide 12: Pin Description – Top Level
No. | Name of Pin | No. of Pins | Direction | Description
1. | Write Data | 8 | Input | Input data to SRAM
2. | Read Data | 8 | Output | Output data from SRAM
3. | Write Enable | 1 | Input | Enable write operation
4. | Read Enable | 1 | Input | Enable read operation
5. | Write Clock | 1 | Input | Clock for write operation
6. | Read Clock | 1 | Input | Clock for read operation
7. | Reset | 1 | Input | To reset FIFO memory
8. | Flag Logic | 4 | Output | Show status of FIFO

## Slide 13: Important consideration in design
Overflow:
  Occurs when the FIFO is full and writer attempts to insert a new data element
Underflow:
  Occurs when the FIFO is empty and reader attempts to retrieves data from buffer

## Slide 14: Write Control Block

## Slide 15: Pin Functions – Write Control Block
No. | Name of Pin | No. of Pins | Direction | Function
1. | f_full | 1 | Input | Disable signal to write operation
2. | reset_n | 1 | Input | To reset write Pointer
3. | wr_clk | 1 | Input | Clock for write operation
4. | b_wr_ptr | 10 | Output | Output address to SRAM
5. | MSB_wr_ptr | 1 | Output | To generate flag logic

## Slide 16: Write Control Block - RTL

## Slide 17: Test Cases- Writing data
reset_n = 0, wr_clk= x, f_full=x : O/P wr_ptr = 3’b000;
reset_n = 1, wr_clk= pos , f_full=1 : O/P wr_ptr = Prev_value;
reset_n = 1, wr_clk= pos, f_full=0 : O/P wr_ptr = +1’b1;

## Slide 18: Write Control Block – Simulation Results

## Slide 19: Read Control Block

## Slide 20: Pin Functions – Read Control Block
No. | Name of Pin | No. of Pins | Direction | Function
1. | f_empty | 1 | Input | Show status of FIFO as empty
2. | reset_n | 1 | Input | To reset read Pointer
3. | rd_clk | 1 | Input | Clock for read operation
4. | b_rd_ptr | 10 | Output | Output address to SRAM
5. | MSB_rd_ptr | 1 | Output | To generate flag logic

## Slide 21: Read Control Block – RTL

## Slide 22: Test Cases – Reading data
reset_n = 0, rd_clk= x, f_empty=x : O/P read_ptr = 3’b000;
reset_n = 1, rd_clk= pos , f_empty=1 : O/P read_ptr = Prev_value;
reset_n = 1, rd_clk= pos, f_empty=0 : O/P read_ptr = +1’b1;

## Slide 23: Read Control Block – Simulation Results

## Slide 24
Dual Port SRAM – Top Level Diagram

## Slide 25: Pin Description – Dual Port SRAM
No. | Name of Pin | No. of Pins | Direction | Function
1 | b_rd_ptr | 10 | Input | Port specifying the read address
2 | b_wr_ptr | 10 | Input | Port specifying the write address
3 | wr_data_in | 8 | Input | Input data port
4 | rd_clk | 1 | Input | Read clock signal for operation
5 | wr_clk | 1 | Input | Write clock signal for operation
6 | rd_en_in | 1 | Input | Enable pin for the read operation
7 | wr_en_in | 1 | Input | Enable pin for the write operation
8 | rd_data_out | 8 | Output | Output data port

## Slide 26: Dual Port SRAM - RTL

## Slide 27: Dual Port SRAM – Simulation Results

## Slide 28: Synchronizers
Synchronizer
Synchronizer
wr_clk
rd_clk
rd_ptr
syn_rd_ptr
wr_ptr
syn_wr_ptr

## Slide 29: Synchronizer – Top Level and RTL Diagram

## Slide 30: Pin Functions – Synchronizers
No. | Name of Pin | No. of Pins | Direction | Function
1. | wr_ptr | 10 | Input | Address to be synchronized
2 | rd_ptr | 10 | Input | Address to be synchronized
3 | wr_clk | 1 | Input | Synchronizing clock
4 | rd_clk | 1 | Input | Synchronizing clock
5 | sync_wr_ptr | 10 | Output | Synchronized address
6 | sync_rd_ptr | 10 | Output | Synchronized address

## Slide 31: Gray to Binary Converter - RTL

## Slide 32: Binary to Gray Converter - RTL

## Slide 33: Flag logic block

## Slide 34: Pin Functions – Flag Logic
No. | Name of Pin | No. of Pins | Direction | Function
1. | b_wr_ptr | 10 | Input | Address input to comparator
2. | b_rd_ptr | 10 | Input | Address input to comparator
3. | Config_depth | 10 | Input | Limiting value of memory location
4. | Reset_n | 1 | Input | To set empty flag
5. | wr_clk | 1 | Input | To synchronize Read pointer
6. | rd_clk | 1 | Input | To synchronize Write pointer
7. | f_full | 1 | Output | Show status as FIFO is Full
8. | f_empty | 1 | Output | Show status as FIFO is empty
9. | f_almost _full | 1 | Output | FIFO is Almost empty
10. | f_almost_empty | 1 | Output | FIFO is Almost empty

## Slide 35: Flag logic block –RTL

## Slide 36: Flag logic block-Simulation

## Slide 37: Test Cases- Top Level RTL
reset_n =0 ; wr_en=x , rd_en = x : FIFO reset
reset_n =1 ; wr_en=1 & f_full = 0 , rd_en = 0 : FIFO write operation (b_wr_ptr= +1’b1)
reset_n =1 ; wr_en=0 , rd_en = 1 & f_empty = 0 : FIFO read operation (b_rd_ptr= +1’b1)
reset_n =1 ; wr_en=1 , rd_en = 1 : Async read & write

## Slide 38: Top Level– Simulation Results

## Slide 39: Top Level– Simulation Results

## Slide 40: Top Level– Simulation Results

## Slide 41: Applications
Packet Buffering :
  Data written into the FIFO can be stored until the system on the output of the FIFO is ready to accept the data.
Frequency coupling:
  FIFO provides frequency coupling, taking data in at one rate and output the data at another data rate. The input and output data rates of the FIFO being controlled by the discrete Read and Write clock signals.
Bus Matching :
  Data transfer may need to take place between separate digital domains with different bus widths. Here the FIFO acts as a bridge between the domains, channeling the data from the input of a particular bus width , to the output with another bus width.

## Slide 42: Advantages
Data Rate Matching.
Buffering and bus matching parallel FIFO structure allow formulation of any word size while serial FIFO structure provide a rapid and simple like other structure.
Interchip communication protocol problem is solved by FIFO.

## Slide 43: Disadvantages
Noise in signals is caused by switching operation and alteration of memory content.
Synchronization circuit is required to synchronize WRITE CLOCK and READ CLOCK

## Slide 44: Thank you…!